## Slide 1: Design of Digital Circuits Lecture 7.1: Sequential Logic Design II
Prof. Onur Mutlu
ETH Zurich
Spring 2019
14 March 2019

## Slide 2: Agenda for This Week
Today
  Wrap up Sequential Logic
  Hardware Description Languages and Verilog
    Combinational Logic
    Sequential Logic
Tomorrow
  Timing and Verification

## Slide 3: Agenda for Next Week
Thursday
  Von Neumann Model of Execution
  Instruction Set Architecture
    LC-3 and MIPS
Friday
  ISA and Assembly Programming

## Slide 4: Extra Assignment 1: Lecture Video
Why study computer architecture?
Why is it important?
Future Computing Architectures
Required Assignment
  Watch my inaugural lecture at ETH and understand it
  https://www.youtube.com/watch?v=kgiZlSOcGFM
Optional Assignment – for 1% extra credit
  Write a 1-page summary of the lecture
    What are your key takeaways?
    What did you learn?
    What did you like or dislike?
    Upload PDF file to Moodle – Deadline: Friday, March 15.

## Slide 5: Extra Assignment 2: Moore’s Law (I)
Paper review
G.E. Moore. "Cramming more components onto integrated circuits," Electronics magazine, 1965
Optional Assignment – for 1% extra credit
  Write a 1-page review
  Upload PDF file to Moodle – Deadline: Friday, March 22
I strongly recommend that you follow my guidelines for (paper) review (see next slide)

## Slide 6: Extra Assignment 2: Moore’s Law (II)
Guidelines on how to review papers critically
  Guideline slides: pdf ppt
  Video: https://www.youtube.com/watch?v=tOL6FANAJ8c
  Example reviews on “Main Memory Scaling: Challenges and Solution Directions” (link to the paper)
    Review 1
    Review 2
  Example review on “Staged memory scheduling: Achieving high performance and scalability in heterogeneous systems” (link to the paper)
    Review 1

## Slide 7: Required Readings (This Week)
Hardware Description Languages and Verilog
  H&H Chapter 4 in full
Timing and Verification
  H&H Chapters 2.9 and 3.5 + (start Chapter 5)
By tomorrow, make sure you are done with
  P&P Chapters 1-3 + H&H Chapters 1-4

## Slide 8: Required Readings (Next Week)
Von Neumann Model, LC-3, and MIPS
  P&P, Chapters 4, 5
  H&H, Chapter 6
  P&P, Appendices A and C (ISA and microarchitecture of LC-3)
  H&H, Appendix B (MIPS instructions)
Programming
  P&P, Chapter 6
Recommended: Digital Building Blocks
  H&H, Chapter 5

## Slide 9: Wrap-Up Sequential Logic Circuits and Design

## Slide 10: Circuits that Can Store Information

## Slide 11: The Gated D Latch

## Slide 12: Sequential Logic Circuits

## Slide 13: Review: Finite State Machines

## Slide 14: Recall: Finite State Machines (FSMs)
Each FSM consists of three separate parts:
  next state logic
  state register
  output logic
state register
At the beginning of the clock cycle, next state is latched into the state register

## Slide 15: Recall: Finite State Machine Example
“Smart” traffic light controller
  2 inputs:
    Traffic sensors: TA , TB (TRUE when there’s traffic)
  2 outputs:
    Lights: LA , LB (Red, Yellow, Green)
  State can change every 5 seconds
    Except if green and traffic, stay green
From H&H Section 3.4.1

## Slide 16: Recall: FSM Transition Diagram
Moore FSM: outputs labeled in each state
  States: Circles
  Transitions: Arcs

## Slide 17: Recall: Finite State Machine: State Transition Table

## Slide 18: Recall: FSM State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S’1 | S’0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11

## Slide 19: Recall: FSM State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S’1 | S’0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
S’1 = S1 xor S0 (Simplified)
S’0 = (S1 ∙ S0 ∙ TA) + (S1 ∙ S0 ∙ TB)

## Slide 20: Recall: Finite State Machine: Output Table

## Slide 21: Recall: FSM Output Table
Current State |  | Outputs | 
S1 | S0 | LA | LB
0 | 0 | green | red
0 | 1 | yellow | red
1 | 0 | red | green
1 | 1 | red | yellow
Output | Encoding
green | 00
yellow | 01
red | 10
70

## Slide 22: Recall: FSM Output Table
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
LA1 = S1
LA0 = S1 ∙ S0
LB1 = S1
LB0 = S1 ∙ S0

## Slide 23: Recall: Finite State Machine: Schematic

## Slide 24: Recall: FSM Schematic: State Register

## Slide 25: Recall: FSM Schematic: State Register

## Slide 26: Recall: FSM Schematic: Next State Logic
S’1 = S1 xor S0
S’0 = (S1 ∙ S0 ∙ TA) + (S1 ∙ S0 ∙ TB)

## Slide 27: Recall: FSM Schematic: Output Logic
LA1 = S1
LA0 = S1 ∙ S0
LB1 = S1
LB0 = S1 ∙ S0

## Slide 28: Recall: FSM Timing
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB
See H&H Chapter 3.4

## Slide 29: Finite State Machine: State Encoding

## Slide 30: FSM State Encoding
How do we encode the state bits?
  Three common state binary encodings with different tradeoffs
    Fully Encoded
    1-Hot Encoded
    Output Encoded
Let’s see an example Swiss traffic light with 4 states
  Green, Yellow, Red, Yellow+Red

## Slide 31: FSM State Encoding (II)
Binary Encoding (Full Encoding):
  Use the minimum number of bits used to encode all states
    Use log2(num_states) bits to represent the states
  Example states: 00, 01, 10, 11
  Minimizes # flip-flops, but not necessarily output logic or next state logic
One-Hot Encoding:
  Each bit encodes a different state
    Uses num_states bits to represent the states
    Exactly 1 bit is “hot” for a given state
  Example states: 0001, 0010, 0100, 1000
  Simplest design process – very automatable
  Maximizes # flip-flops, minimizes next state logic

## Slide 32: FSM State Encoding (III)
Output Encoding:
  Outputs are directly accessible in the state encoding
  For example, since we have 3 outputs (light color), encode state with 3 bits, where each bit represents a color
  Example states: 001, 010, 100, 110
    Bit0 encodes green light output,
    Bit1 encodes yellow light output
    Bit2 encodes red light output
  Minimizes output logic
  Only works for Moore Machines (output function of state)

## Slide 33: FSM State Encoding (III)
Output Encoding:
  Outputs are directly accessible in the state encoding
  For example, since we have 3 outputs (light color), encode state with 3 bits, where each bit represents a color
  Example states: 001, 010, 100, 110
    Bit0 encodes green light output,
    Bit1 encodes yellow light output
    Bit2 encodes red light output
  Minimizes output logic
  Only works for Moore Machines (output function of state)
The designer must carefully choose
an encoding scheme to optimize the design under given constraints

## Slide 34: Moore vs. Mealy Machines

## Slide 35: Recall: Moore vs. Mealy FSMs
Next state is determined by the current state and the inputs
Two types of finite state machines differ in the output logic:
  Moore FSM: outputs depend only on the current state
  Mealy FSM: outputs depend on the current state and the inputs

## Slide 36: Moore vs. Mealy FSM Examples
Alyssa P. Hacker has a snail that crawls down a paper tape with 1’s and 0’s on it.
The snail smiles whenever the last four digits it has crawled over are 1101.
Design Moore and Mealy FSMs of the snail’s brain.

## Slide 37: Moore vs. Mealy FSM Examples
Alyssa P. Hacker has a snail that crawls down a paper tape with 1’s and 0’s on it.
The snail smiles whenever the last four digits it has crawled over are 1101.
Design Moore and Mealy FSMs of the snail’s brain.

## Slide 38: State Transition Diagrams
What are the tradeoffs?

## Slide 39: FSM Design Procedure
Determine all possible states of your machine
Develop a state transition diagram
  Generally this is done from a textual description
  You need to 1) determine the inputs and outputs for each state and 2) figure out how to get from one state to another
Approach
  Start by defining the reset state and what happens from it – this is typically an easy point to start from
  Then continue to add transitions and states
  Picking good state names is very important
  Building an FSM is like programming (but it is not programming!)
    An FSM has a sequential “control-flow” like a program with conditionals and goto’s
    The if-then-else construct is controlled by one or more inputs
    The outputs are controlled by the state or the inputs
  In hardware, we typically have many concurrent FSMs

## Slide 40: What is to Come: LC-3 Processor

## Slide 41: What is to Come: LC-3 Datapath

## Slide 42: Design of Digital Circuits Lecture 7.1: Sequential Logic Design II
Prof. Onur Mutlu
ETH Zurich
Spring 2019
14 March 2019

## Slide 43: Backup Slides: Different Types of Flip Flops

## Slide 44: Enabled Flip-Flops
Inputs: CLK, D, EN
  The enable input (EN) controls when new data (D) is stored
Function:
  EN = 1: D passes through to Q on the clock edge
  EN = 0: the flip-flop retains its previous state

## Slide 45: Resettable Flip-Flop
Inputs: CLK, D, Reset
  The Reset is used to set the output to 0.
Function:
  Reset = 1: Q is forced to 0
  Reset = 0: the flip-flop behaves like an ordinary D flip-flop

## Slide 46: Resettable Flip-Flops
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop (see Exercise 3.10)
Synchronously resettable flip-flop?

## Slide 47: Settable Flip-Flop
Inputs: CLK, D, Set
Function:
  Set = 1: Q is set to 1
  Set = 0: the flip-flop behaves like an ordinary D flip-flop

## Slide 48: Recall: Combinational Logic Blocks

## Slide 49: Recall: Combinational Building Blocks
Combinational logic is often grouped into larger building blocks to build more complex systems
Hides the unnecessary gate-level details to emphasize the function of the building block
We now look at:
  Decoders
  Multiplexers
  Full adder
  PLA (Programmable Logic Array)

## Slide 50: Recall: Decoder
n inputs and 2n outputs
Exactly one of the outputs is 1 and all the rest are 0s
The one output that is logically 1 is the output corresponding to the input pattern that the logic circuit is expected to detect

## Slide 51: Recall: Multiplexer (MUX), or Selector
Selects one of the N inputs to connect it to the output
Needs log2N-bit control input
2:1 MUX

## Slide 52: Recall: Multiplexer (MUX)
The output C is always connected to either the input A or the input B
  Output value depends on the value of the select line S
Your task: Draw the schematic for an 8-input (8:1) MUX
  Gate level: as a combination of basic AND, OR, NOT gates
  Module level: As a combination of 2-input (2:1) MUXes

## Slide 53: Recall: Sequential Logic Blocks

## Slide 54: Recall: An FSM Consists of:
Sequential circuits
  State register(s)
    Store the current state and
    Load the next state at the clock edge
Combinational Circuits
  Next state logic
    Determines what the next state will be
  Output logic
    Generates the outputs
Notes: discuss DFlipFlop here. Latch doesn't do this, so we need sequential circuit that stores state and loads next state at the clock edge. next state is available for the full clock cycle
now lets take a look at this.

## Slide 55: Recall: The Problem with Latches
Currently, we cannot simply wire a clock to WE of a latch
  When the clock is high Q will not take on D’s value AND
  When the clock is low the latch will propagate D to Q
D
Q
CLK = WE
CLK:
0
1
Input:
Output:
Recall the
Gated D Latch
How can we change the latch, so that
1) D (input) is observable at Q (output)
only at the beginning of next clock cycle?
2) Q is available for the full clock cycle

## Slide 56: Recall: The D Flip-Flop
1) state change on clock edge, 2) data available for full cycle
D Latch (Slave)
D Latch (Master)
D
Q
CLK
When the clock is low, master propagates D to the input of slave (Q unchanged)
Only when the clock is high, slave latches D (Q stores D)
  At the rising edge of clock (clock going from 0->1), Q gets assigned D
CLK:
0
1

## Slide 57: Recall: The D Flip-Flop
1) state change on clock edge, 2) data available for full cycle
At the rising edge of clock (clock going from 0->1), Q gets assigned D
At all other times, Q is unchanged
CLK:
0
1
CLK
D
Q
Q
__
D Flip-Flop

## Slide 58: Recall: The D Flip-Flop
At the rising edge of clock (clock going from 0->1), Q gets assigned D
At all other times, Q is unchanged
CLK:
0
1
CLK
D
Q
Q
__
D Flip-Flop
We can use these Flip-Flops
to implement the state register!